## Slide 1: Latest Developments in the IETF Routing AREA
Adrian Farrel
IETF Routing Area Director afarrel@juniper.net adrian@olddog.co.uk
AUSNOG, Sydney, September 2013

## Slide 2: Latest Developments in the IETF Routing Area
  Objectives
    Introduce some of the newer ideas in the Routing Area
    Get you interested enough to read and comment on the work
  Non-objectives
    Discuss IETF things outside the Routing Area
    Cover anything old or established
    Cover everything new
    Go into much detail
    Explain what Juniper is doing or thinks about this stuff
  Me…
    One of two Routing Area Directors
    One of 15 Area Directors on the Internet Engineering Steering Group
    Funded by Juniper Networks
      …but these are just my views

## Slide 3: Agenda
Security and Privacy
  How can the routing infrastructure contribute to network security and privacy?
Interface to the Routing System
  Wouldn’t it be nice if I had a standardised way to talk to the routing infrastructure?
Source Routing
  What can we achieve if each packet carries information about its planned path through the network?
Service Chaining
  How can we enable network function virtualisation and what is the interaction with routing?
How to Participate in the IETF
  What can you do and how do you get involved?

## Slide 4: Security and Privacy

## Slide 5: Security and Privacy
Who cares and why do they care?
  The main concern seems to be the stability of the global routing system
    Route hijacks
    Fat fingers
      “99% of mis-announcements are accidental originations of someone else’s prefix” Randy Bush quoting Google, UU, IIJ, et al.
  Security of internal protocols (IGP, MPLS, etc.) “less of a concern”
    ACLs make it harder to inject
    Stability of routing is of value to attackers!
  Security and privacy are beginning to be taken seriously post-PRISM
    Making it harder (more expensive) to snoop
    Hiding who is talking to whom

## Slide 6: Security and Privacy – What is the IETF Doing?
SIDR
  Working specifically on vulnerabilities in the inter-domain routing system
    Is an Autonomous System (AS) authorized to originate an IP prefix?
    Is the AS-Path represented in the route the same as the path through which the NLRI travelled?
  Not new work, and becoming mature
    19 RFCs on RPKI and Origin Validation
    Examining additional security features for BGP
  Questions are now about adoption and deployment
KARP
  Investigating security vulnerabilities in core routing protocols
    Identifying areas for work – devolved to the protocol working groups
    Formulating “best practices”
  Also not new work, and no surprises
    Clear text passwords and MD5 are not too clever
    TCP-AO would be good to use
    There are some holes around Discovery and Hello mechanisms
    Automatic key rotation is missing and might not be wanted
PERPASS
  A new mailing list for discussion of privacy

## Slide 7: Interface to the
Routing System

## Slide 8: Why Interface to the Routing System (I2RS)
SDN focuses on programming the data plane
  Switch programming (cross-connects)
  Forwarding (FIB)
There are many functions and features not covered by SDN
  Control of routers
  Control of routing protocols
  Management of the “routing system”
Existing techniques are non-standard
  Using CLI to achieve these functions is very frustrating
  Expensive, time-consuming, error-prone, risky
Need for a standard approach
  Strong desire for a simple and standard approach

## Slide 9: I2RS Architecture
Forwarding Plane
FIB
RIBs and RIB Manager
Policy DB
Routing and Signaling Protocols
Topology DB
OAM, Events and Measurement
I2RS Agent
I2RS Client
I2RS Client
Router
Server
Application
Application
Application
I2RS Protocol & Data Encoding

## Slide 10: Simple Use Cases for I2RS
Use cases are being driven by conversations with operators
  Only working on ideas that operators want to deploy soon
Reality of use cases depends on vendors’ implementations
  Some functions are easier to achieve than others!
  Starting with simple use cases that can be achieved easily and which will make significant difference to operational practices
Current work is to net down to a few key use cases
  Programming and managing the RIB
  BGP use cases
  Traffic steering and classification
  DDoS mitigation
  Topology reading, monitoring, and control
  Service chaining

## Slide 11: I2RS – Programming and Managing the RIB
Read/write data in the RIB
  Routes installed
  Candidate routes for different purposes
    IP
    Multicast
    MPLS
  RIB Tables
RIB change notifications (on specific filters)
Read-only data from FIB
  Prefix + next-hop for verification of FIB programming
Optimizing exit control
  Route traffic from a network device to a given edge device / interface based on business logic
Control outgoing encapsulation
  IP, GRE, MPLS, etc.

## Slide 12: I2RS – BGP Use Cases
Troubleshooting and Analysis of BGP
  Route reachability, Expected exit points
  Route hijacking detection, Route stability analysis and damping
  Reporting routes dropped (Policy based, Malformed, etc)
  Reporting damped/unstable routes
  Protocol statistics
Performance Based Routing
  Compute least delay exit paths, least cost exit paths
  Assure SLAs
  Reduce jitter and RTT of data plane
  Spread utilization of external links
BGP configuration
  Centralize BGP policy
  VPN provisioning and stitching
Advanced BGP uses
  Service chaining (requires protocol updates)
  Route manipulation

## Slide 13: I2RS – What work is Needed?
Architecture
  Now a working group draft
Use Cases
  Converging on some key cases
Information Models
  Work well progressed on RIB information model
Requirements
  Requirements for Data Encoding Language(s)
    Parsable, extensible, recursion, programmable
  Requirements for Data Exchange Protocol(s)
    Non-blocking transactions, stateless, duplex, multi-channel
Protocol Choices and Extensions
  Encoding candidates YANG, XML, ForCES schema, JSON, SMI
  Protocol candidates Netconf, XMPP, HTTP, COAP, ForCES, IPFIX
  Work to be done in the appropriate working group
Data Models

## Slide 14: Source Routing

## Slide 15: Source Routing – An Overloaded Term
IP Source Routing
  A list of IP hops to traverse
  IPv4 Options for Loose and Strict Source Routes
    Only 9 hops, don’t cross AS boundaries, not used
  IPv6 Source Route
    Deprecated!
Source-aware Routing
  Hop-by-hop routing decisions take account of source as well as destination
  A form of policy-based routing
Source-based Classification to a Tunnel
  A concept applying to any tunnelling and especially MPLS
  Packets are labelled and then follow an LSP
Explicit Routing
  A term usually associated with MPLS-TE path establishment
  Packets follow the path of a pinned LSP

## Slide 16: Source Routing – IGP Labels
Suppose:
  Every router in a IGP domain creates 1-hop LSPs to its IGP neighbors
  For each such neighbor advertise the label in the IGP
  Flood to everyone in the IGP domain the label used by the LSP terminating at the neighbor (as well as the identity of the neighbor)
  Label effectively identifies a neighbor or even an interface

## Slide 17: IGP Labels - Consequences
A source node can impose a path by using a label stack
Can be used to describe an arbitrary number of paths in the network
Potential uses
  Per-micro-flow traffic engineering
  Signaling-free (state-free) traffic engineering
  Fast reroute
  Directed OAM
Concerns and limitations
  How big is the label stack?
  Interaction with special-purpose labels?
  Path computation requirements?
No change to the data plane

## Slide 18: IGP Labels : EXAMPLE For EXPLICIT paths

## Slide 19: Source Routing – TUNNELS AS LABELS
Existing LSPs become “hops”
  LDP or RSVP LSPs
IGP en-queues LSP tail end routes into tunnel RIBs
  I.e., the tunnel provides a forwarding adjacency
Third-party next hop gets set to originating router transport loopback
Label stack construction
  At the head end is a sequence of “hops”
  Is expanded as part of route resolution

## Slide 20: Tunnels As Labels - Example
LDP
301
302
301
300
302
200
100
Example Label Stack

## Slide 21: Tunnels as Labels - Consequences
A source node can impose a path that includes LSPs
Can be used to stitch together different types of LSP
Potential uses
  “Seamless MPLS”
    Extend MPLS to the edge
  Reduce label stack size on long paths
  Distribute responsibility for path computation
  Fast reroute and pre-planned path segments
  Even IGP reachable label paths can be represented
    Models VPNs and BGP reachability
Concerns and limitations
  More complex additions to IGPs or BGP
  More complex management/debug
No change to the data plane

## Slide 22: Source Routing – What is the IETF Doing?
It is really early stages in the IETF for source routing
  A bunch of drafts from Cisco and Juniper
  Lots of interest from service providers
Held a BoF at IETF-87 on “segment routing” called STATUS
  Lots of enthusiasm
  Some oceans were boiled
The STATUS email list is active
  Discussing drafts and technology
  Trying to focus towards a working group
Likely to meet at IETF-88 as a BoF or a Working Group
  Scoped to architecture and use cases?
  Technology independent?
  IPv6 in or out of scope?

## Slide 23: Service Chaining

## Slide 24: Service Chaining – Problem Statement
Today’s workloads consist of multi-tiered applications
  Multiple distributed entities (e.g., Web server, load balancers, data base servers, etc.) cooperate to provide a service
Individual workload components communicate with each other in carefully defined ways
  Traffic between components is required (by policy) to flow through specialized network services (e.g., firewalls, IDS, etc.)
  Resultant communication flows are modelled as “service chains”
Today, steering of traffic between services within a service chain is achieved via L2/L3 data plane forwarding
  Complex and difficult to automate
  Predicted scaling challenges
Current network service deployment models are generally static, hard to manipulate (create, move, destroy)
Currently no (efficient) way to share information between the network and services, or among services in a chain
Virtual platforms require an agile service insertion model
  With horizontal/vertical scaling requirements
Source: after Guichard and Narten (IETF-87)

## Slide 25: Service Chaining – model
Services provided off-path by physical or virtual service nodes
Packets diverted through tunnels
  Return to forwarding path
    By tunnel
    Via forwarding
    After attention by other service nodes
Shortest path
Tunnel
Forwarding path

## Slide 26: Service Chaining - Questions
What services are we talking about?
At what level is service chaining applied?
  Per transaction
  Per flow
  Per packet
How is the service chain determined?
  By operators / planning tools
  By the service nodes themselves
Where is the chain of services encoded?
  In configuration at the service nodes
  In messages in the transactions/flows
  In per-packet data
Is this really a data centre / virtualization problem?
How do service nodes exchange information?
  Why would they want to?
  What are the security implications?
  Is there a communications protocol?
  Do we need meta-data in packets?

## Slide 27: Service Chaining – What is the IETF Doing?
It is really early stages in the IETF for service chaining
  A bunch of drafts from Cisco and Huawei
  Lots of interest from network operators
Held a BoF at IETF-87 on “network service chaining” called NSC
  Limited to presentations of use cases by network operators
  Lots of enthusiasm
  Focus and common use of terms was absent
The NSC email list is active
  Discussing drafts and terminology
  Trying to focus scope towards another BoF at IETF-88
    Intent is to make this WG-forming
Issues of overlap with other work
  I2RS?
  Source Routing?
  ALTO?

## Slide 28: How To Participate in the IETF

## Slide 29: How Does the IETF Work?
The IETF is an open standards organisation
  All standards documents are freely downloadable
  Participation is open to everyone
  Work in progress is openly accessible
Standards gestate as internet-Drafts
  Anyone can write and post an Internet-Draft
Work is broken up into broad topics
  A working group for each topic
  Governed by a charter with deliverables
The work is done predominantly by email
  Mailing list for each working group
    Anyone can subscribe
  Review and discussion of Internet-Drafts
Face-to-face meetings three times per year
  Useful for high-bandwidth communications
  Attendance is far from essential

## Slide 30: How Can you Contribute to the IETF?
Participation by network operators is particularly welcomed
  Some operators are quite active (Orange, DT, Google, …)
  Internet Engineering Providers Group (IEPG)
    Informal meeting before every IETF meeting
Things to do…
  Subscribe to mailing lists and read the threads
  Read Internet-Drafts and comment on them
    In private to the authors if you are shy 
    Make editorial or technical comments
  Initiate work you care about
    Send mail
    Write an Internet-Draft
    Ask vendors to work with you
  Ask an Area Director for help

## Slide 31: Questions? afarrel@juniper.net adrian@olddog.co.uk