## Slide 1: Virtualising The Network with Cloud-based CPE
Tim Nagy
AusNOG 2013 – 6 September 2013

## Slide 2: CHALLENGES WITH TODAY’S FIXED SERVICE ARCHITECTURE
New Services = additional CPE functionality
  CPE is low margin resale
  Higher function, or more CPE increases CAPEX
  Increased complexity of CPE increases OPEX
  Complexity increases probability of poor user experience
Stalled Service Innovation
  A Site / Location / Line = A Customer
  No visibility of end devices, user sessions & state
  High touch upgrades impede new service rollout
  Proliferation of OTT substitutes = “the invisible cloud”
Increasing CAPEX
Increasing OPEX
Service Margin
Increasing Churn
Slow Service Innovation
Service Revenue
Today’s Fixed Service Architecture
is heavily dependent upon high-function CPE devices
that present challenges to the Service Provider Business Model

## Slide 3: The concept of Cloud-Based CPE
DHCP
Firewall
Routing / IP Forwarding
NAT
Modem / ONT
Switch
Access Point
Voice
MoCA/ HPAV/ HPNA3
Typical CPE Functions
DHCP
FW
Routing / IP Forwarding
NAT
Modem / ONT
Switch
Access Point
Voice
MoCA/ HPAV/ HPNA3
Simplified L2 CPE
A Simplified CPE
  Remove CPE barriers to service innovation
  Lower complexity & cost
In Network CPE functions
  Leverage & integrate with other network services
  Centralize & consolidate
  Seamlessly integrate with mobile & cloud based services
Direct Connect
  Extend reach & visibility into the home
  Per device awareness & state
  Simplified user experience
  Simplify the device required on the customer premise
  Centralize key CPE functions & integrate them into the network edge
BNG / PE in SP Network

## Slide 4: COMPARING TODAY’S CPE WITH CLOUD CPE
Service Oriented
Feature Oriented
Abstracted
Localized
Elastic Resources
Static Capacity
Physical CPE
Cloud CPE
Functionality Rich
Single Management Touch point
Site & Device Visibility
Demarcation Wall
High Touch Operations
Internalized Management
Linear Costs
Marginal Costs
Extensible Capability
Hardcoded Capability

## Slide 5: Business Services – Potential Applications
Business Services | Machine to machine applications
 | Building Automation
Business Applications | Unified Communications as a Services
 | Productivity & Storage – Software as a Service
VPN Light | Secure access for remote users
 | Cost effective VPN services for Branches & Retail sites
Secure Business Internet | Clean Pipes
 | Managed Firewall

## Slide 6: Vision for Cloud-based CPE End-to-end solution for moving services and value into the cloud
Today
Cloud-CPE solution
Full featured CPE
Service Provider IP Edge
Internet
HQ DC
Data Center
Service Provider CO/PoP/DC
or
Enterprise HQ/DC
“Cloud-Connect” CPE
Modem / ONT
Switch
Access Point
Voice
DHCP
Routing
CGNAT
VPN
Modem / ONT
Switch
Voice
DHCP
Routing
NAT
FW & UTM
Management
Wireless Controller
FW & UTM
Wireless Controller
Premises Security + Automation
Management
Deep Inspection/ Monitoring
Storage
Business Apps
User/Role
Awareness
Notes: Today’s Fixed Service Architecture is heavily dependent upon high function CPE devices that also present challenges to the Service Provider Business Model. With this CPE centric model service innovation often requires additional that functionality be added to the CPE directly increasing its cost and complexity. Furthermore, functions such as NAT in the CPE prevent Service Provider visibility to the number and type of attached devices in the home – in essence a subscriber is equal to an entire household. Conversely in the mobile service architecture, where service creativity and velocity are evident, each device is directly attached and completely visible to the Service Provider network. Because of its lack of visibility & control service innovation is stalled from a creativity standpoint and the requirements to introduce new features and functions into millions of deployed CPE devices significantly impacts service velocity, not to mention the increased CAPEX and OPEX costs associated with acquiring higher function CPE devices, CPE replacements and sw upgrades and increase cost of managing millions of complex devices in homes and small businesses.
Juniper can disrupt the BB CPE market with a simplified architecture – by moving key CPE functions into the cloud integrating them into the network & monetize as SW and as a result simplify the device in the home to provide nothing more than connectivity. This simplifies & improves the user experience, and improves the economics of networking by removing CPE service innovation barriers, provided visibility to all attached devices, and leveraging & integrating with other network services.

## Slide 7: CLOUD CPE ARCHITECTURE HIGH LEVEL COMPONENTS
Customer Site
vCPE Context
Onsite CPE
Services
Management
Edge Router
Access & Aggregation
Simplified CPE device with switching, access point, upstream QoS and WAN interfaces
Optional L3 and Tunneling
  CPE specific context in router
  Layer 3 services (addressing & routing)
  Basic value services (NAT, Firewall,…)
  Advanced security services (UTM, IPS, Firewall,…)
  Extensible to other value added services (M2M, WLAN, Hosting, Business apps,…)
  Cloud based
  Provisioning
  Monitoring
  Customer Self-care
Notes: 7
With this new service architecture it becomes simple to blend in home and in cloud services to offer unique & innovative consumer services. For example Universal Plug and Play (UPnP) is used in the home to support zero-configuration, "invisible" networking, and automatic discovery for a breadth of device categories from a wide range of vendors. This means a device can dynamically join a network, obtain an IP address, convey its capabilities, and learn about the presence and capabilities of other devices.
By implementing the My Home VPN service the this same construct can be used to enable new services that are cloud based. A service provider could implement a portal where consumers could subscribe to services offered in the cloud. Once subscribed to, the service is connected to the My Home VPN and using UPnP devices connected in the home can dynamically discover, access and consume the cloud based services as if they were deployed and available directly in the home.

## Slide 8: CLOUD CPE FOR BROADBAND SUBSCRIBERS “NETWORK ENRICHED RESIDENTIAL GATEWAY” (BBF)
In Home Services ↔ My Home VPN ↔ SP Cloud Services
Connectivity / Smart Switching
Wireless AP
Zero Touch Provision
802.1 p/q
Layer 2 CPE
Enhanced Visibility, Control & Service Innovation at a Fraction of Costs for Existing L3 CPE Service Architecture
Cloud CPE
Routing (IP Forwarding), SFW NAT, DHCP Server/Relay, UPnP Proxy/Relay
Dynamic Service Activation via RADIUS / DHCP interaction
Dynamic VLAN Assignment
Dynamic Policy & Profiles; QoS, Accounting, Traffic Mgmt
Captive Portal Redirection
My Home VPN services
Tunnel Termination
TR69 Agent
Wii
SP Data Center
Internet
Mobile/Remote VPN Members
C-CPE Context
Public/Private IP Address Domain
Private IP Address Domain
Management & Self-care
Notes: The cloud CPE solution architecture includes the Layer 2 CPE deployed in the home offering switched connectivity between devices and access to the cloud and Internet via a WAN connection to the service provider access network. DHCP services, NAT and IP Forwarding are provided by the Cloud CPE context on the MX platform. There is one Cloud CPE context per household. The cloud CPE context can also be incorporated with Junos VPN services to create the My home VPN which can be used to create a unique blend of in home and in cloud services. These services can be consumed from within the home of from any Internet enabled connection with secure access from a Junos Pulse enabled device. This disruptive service architecture provides a flexible platform offering enhanced visibility, control and innovation at a faction of the cost of today’s CPE centric architecture.

## Slide 9: BROADBAND DEVICE VISIBILITY EXAMPLE: PARENTAL CONTROL BASED ON DEVICE POLICIES
HOME NETWORK
Laptop
L2 Bridge
Tablet
Little Jimmy’s Desktop
ACTIVITY REPORTING
Volumes
Content
Facebook.com
Twitter.com
Hulu.com
Wikipedia.com
Iwishiwere21.com
Portal / Mobile App
Self-care & Reporting
CONTENT FILTER
You have tried to access www.iwishiwere21.com
This site is filtered in order to protect you
TIME OF DAY
Internet access from this device is not permitted between 7pm and 7am.
Try again tomorrow
Notes: 9

## Slide 10: BUSINESS CLOUD CPE CO/POP Centric Architecture (PE)
…
Wireless L2 Bridge
SOHO, SMB, Branch
DSL or PON, Cable
Cell Sites
Mobile Terminals
Mobile
Backhaul
SMB, Branch
Enterprise
DSL or PON, Cable
TDM, Ethernet
TDM, Ethernet
Identity GW
Cloud-Connect or Router
vIdentity Server
Service Complex/VA
CO / PoP
Mega PoP / Data-Center
Service-
Eng’d Paths
(SEP)
Wireless L2 Bridge
Residence,
Home
4G SMB,
Branch
DSL or PON, Cable
…
Service Complex/ VA
SEP
Service Complex optionally placed locally or in centralized/regional Data-Center or Mega-PoP
Cloud-Connect or Router
Data-Center Edge Router
DHCP
Routing
NAT
VPN
Cloud CPE Context
PE Router
Management

## Slide 11: BUSINESS CLOUD CPE DATA CENTER Centric Architecture (PE)
Wireless L2 Bridge
SOHO, SMB, Branch
DSL or PON, Cable
Cell Sites
Mobile Terminals
Mobile
Backhaul
Wireless L2 Bridge
SMB, Branch
Enterprise
DSL or PON, Cable
TDM, Ethernet
TDM, Ethernet
vIdentity GW
Router
vIdentity Server
SP 1
DHCP
Routing
NAT
VPN
Cloud CPE Context
Internet
SP N
Tunnel Through VPN Service
Cloud Branch Router
Cloud Security, etc…
End-Customer Solutions
Enterprise or SP Data Center
Data-Center Edge Router
…
Service Complex / VA
Management

## Slide 12: SERVICE COMPLEX OPTIONS & CONSIDERATIONS
Service Card in Chassis
Virtual Appliance
Cloud Platform
Large Central Office or Point of Presence
Likely integrated with BNG or PE router
Potentially as a Service Gateway or Aggregator
Potential Models
Likely Deployment Location
Considerations
Scale bounded by available router slots
Simplified deployment & operations
Service location dictated by router placement
Longer technology life cycle
Co-located with router platform in large CO or PoP
Centralized in Metro PoP or Data Center
Flexible deployment options
Simple to integrate new x86 technology
Scale incrementally
Multiple boxes - Potential operational issues & conflicts
Centralized in Cloud Data Center
On demand linear scale & multi-tenancy to scale instances)
Requires support of & integration with customer cloud platform
Potential operational conflicts
Potential of in-efficient traffic flow

## Slide 13: FINAL THOUGHT - EXAMPLE OF BUSINESS CASE REVENUE AND COST BENEFIT
3.45
Revenue benefit, $ mn
482.0
2017
16
123.6
14
47.8
13
8.9
2012
0.7
15
248.2
Capex benefit, $ mn
13
2012
14.7
1.4
4.3
7.4
10.4
0.3
2017
16
15
14
Opex benefit, $ mn
15
92.8
16
59.0
2017
14
19.3
37.3
13
5.4
2012
0.9
Margin benefit, % points
2017
16
15
14
13
2012
  Rationale / Description
  Revenue benefit is driven primarily from reduced service churn in cloud CPE model and from new service (My Home VPN )
  Opex benefit comes from reduced volume of support calls related to CPE and service issues (partially offset by increased licensing fees)
  Capex benefit comes from reduced price of CPE equipment and less frequent CPE replacement
  Outcome of business case for a service provider with 9M residential subscribers (DSL and fiber )

## Slide 14: Thank you
Notes: 14